## Slide 1: Update on MPPC frontend electronics development at IU
Gerard Visser

## Slide 2: FEE for UCLA HCAL prototype

## Slide 3: Single MPPC installed (#2 location)
dark noise (+maybe small light leaks)
on @ 72 V
off @ 67 V

## Slide 4: Gang of four MPPC installed
dark noise (+maybe small light leaks)
#2 on @ 72 V, others off @ 67 V
all off @ 67 V
Note the histograms here and following in linear scale

## Slide 5: Gang of four MPPC, one at a time on
#2
#0
#3
#1

## Slide 6: Gang of four MPPC, #2 on vs. all on
#2 on @ 72 V, others off @ 67 V
all on @ 72 V
It all looks pretty reasonable I think
p.s. – all signal volts/div on above slides are wrong by a factor
of 2. too late to correct, and it doesn’t really matter anyway.

## Slide 7: Backup slides

## Slide 8: Requirements for FEE for UCLA W-SciFi calorimeter
FEE fits behind tower (26.7 mm square), and compatible to optical coupling of MPPC’s to light guide
Single analog output signal from tower, representing sum of 4 MPPC
Full scale signal range (whole tower sum) >5,000 pixel with good linearity ≈1%.
Noise level low enough to calibrate via single-pixel peak. (This is necessary to adjust each of 4 MPPC devices to matching gain).
Temperature compensation and bias voltage stability sufficient to have ≈1% gain stability. (Over temperature range 25 to 40°C ?)
  Remark: 1% gain error results from merely ≈0.25 °C uncompensated temperature change.
Low cost, low power, and easy to integrate to large system
(slightly updated from previous meeting)

## Slide 9: FEE block diagram
readout system
regulator
+
DAC
MPPC
DAC
voltage reference
thermistor
+
preamp/ shaper
cable driver
1-wire to I2C bridge hardware
some software on some linux box somewhere

## Slide 10: Control system
local I2C devices
multidrop bus,
unique global address factory programmed
100 kb/s
3.125 kb/s (×2)
 62.5 DAC writes/s
while true; do { echo -ne 'rb5528DC6C920300009544\n' >/dev/ttyUSB0; sleep 0.8; echo -ne 'rb5528E26C920300006B44\n' >/dev/ttyUSB0; sleep 0.8; echo -ne 'rb5528DC6C9203000095BEFFFF\nrb5528E26C920300006BBEFFFF\n' >/dev/ttyUSB0; } done
(for example...)
$29.95 !!
(need ~5 for beam test)